SECTION 09 51 00

HARMONI Acoustic Ceiling Panels

GENERAL

summary

Section Includes:

Lightweight lay-in-applied acoustical ceiling panels.

Related Sections:

edit note:  add or delete sections per project requirements.

Section 09 53 00 – Acoustical Ceiling Suspension Systems.

Section 09 51 00 – Acoustical Ceilings.

Section 09 21 16 – Gypsum Board Assemblies.

Division 21 – Fire Suppression.

Division 23 – Mechanical.  Diffusers, vents, and other mechanical items.

Division 26 – Electrical.  Lights and other ceiling mounted electrical items.

system description

Acoustical Performance Requirements:

NRC (Noise Reduction Coefficient):  Comply with ASTM C423-90a.

SUBMITTALS

Comply with Section 01 33 00 – Submittal Procedures.

Product Data:  Manufacturer’s technical data for each type of panel and baffle including fire-resistive characteristics, finishes, details of installation, and the following:

Manufacturer's installation instructions.

Certified test reports indicating compliance with Performance Requirements specified herein.

Samples:  2 full size sets of Samples of each specified panel for color selection or verification.

Closeout Submittals:  Comply with Section 01 77 00 – Closeout Procedures.

Operating and Maintenance Manual, including cleaning and maintenance instructions.

Extra Material for Owner’s stock.

Material Safety Data Sheets (MSDS).

QUALITY ASSURANCE

Single Source Responsibility:  Obtain panel units for entire Project from a single manufacturer.

Manufacturer's Qualifications:  Firm with not less than Closeout Submittals:  Comply with Section 5 years experience in manufacturing of products similar in complexity to those required for this Project.

Installer's Qualifications:  Firm with not less than 5 years experience in installation of products similar in complexity to those required for this Project, including specific requirements indicated.

Successfully completed not less than 5 comparable scale projects.

DELIVERY, STORAGE, AND HANDLING

Comply with Section 01 60 00 – Product Requirements.

Deliver and store materials in manufacturer's original unopened containers with brands, names, and production lot numbers clearly marked on these containers.

Storage and Protection:  Comply with manufacturer's recommendations.

Store products in a cool, dry place out of direct sunlight.

Protect from elements and from damage.

PROJECT CONDITIONS

Environmental Requirements within building:

Panels do not require special environmental conditions.

Systems may be installed at any stage of construction.

WARRANTY

Provide manufacturer's written warranty per Section 01 77 00 – Closeout Procedures.

Maintenance

Extra Materials:

Deliver not less than the following quantity of each type, color, and pattern of material, exclusive of material required to properly complete installation.

Edit Note:  retain amount of extra materials used on project.  delete this article If no extra materials required or acceptable.

3 percent.

5 percent.

1 carton.

Furnish Extra Materials from same production run to verify run for color.

Package replacement materials with protective covering, identified with appropriate labels.

PRODUCTS

MANUFACTURERS

Subject to compliance with requirements, provide products from the following manufacturer:

pinta acoustic, inc.

2601 49th Avenue North, Ste. 400

Minneapolis, Minnesota  55430

Telephone:	800-662-0032

612-355-4200

Fax:		612-355-4299

Website:	www.pinta-acoustic.com

E-mail:		sales@pinta-acoustic.com

Substitutions:  Comply with Section 01 60 00 – Product Requirements.

manufactured units

Acoustical Ceiling Panels:  Acoustical foam panel consisting of lightweight, open-cell willtec® foam, with applied HPC finish surface:

Density:  0.5 to 0.7 pounds per cubic foot (0.23 to 0.32 kg per m3).

Tensile Strength:  8 psi (0.06 MPa).

Elongation:  8 percent per ASTM D3574-77

Fire resistance:  Class 1 per ASTM E84.

Flame Spread:

Natural:  5.

HPC:  15.

Smoke Density:

Natural:  50.

HPC:  100.

Size:  Nominal 24 inch by 24 inch (610 mm by 610 mm).

Panel Thickness:  2 inch (51 mm) total thickness.

edit note:  select one of the following patterns.  delete designs not required for project.

Patterned Design:  Tartan.

Patterned Design:  Vista.

Edge:  Square Tegular.

Face Finish:  Smooth.

Edit Note:  select panel color below.  delete panel colors not required for project.  HPC improves stain resistance and cleanability.  Minimum orders and longer lead time may apply for custom colors.

Finish:  Provide panels in the following water-based HPC-coated finish:

Finish:  Arctic White.

Finish:  Ivory.

Finish:  Beige.

Finish:  Light Grey.

Finish:  Medium Gery.

Finish:  Dark Grey.

Finish:  Light Blue.

Finish:  Eggshell.

Finish:  Black.

Finish:  Custom color.

Finish:  Premium color.

Sound Absorption Coefficients:  Type E mountings (16 inch air space), ASTM C423-90a.

Frequencies (Hz)	125	250	500	1,000	2,000	4,000	NRC

2 inch:	0.89	0.84	0.78	1.02	1.05	1.00	0.90

Acceptable Product:  HARMONI Acoustical Ceiling Panels.

SUSPENSION SYSTEM

Suspension System:  Refer to Section 09 53 00 – Acoustical Ceiling Suspension Assemblies for acoustical panel support system.

Edit Note:  retain paragraph above or below.  Use Any 15/16 inch or 9/16 inch grid.  15/16 inch grid is recommended by panel manufacturer.

Suspension System:  [Architect to insert acoustical tile ceiling system suspension system specifications here.]

EXECUTION

EXAMINATION

Verification of Conditions:  Examine areas and conditions under which work is to be performed and identify conditions detrimental to proper and or timely completion.

Do not proceed until unsatisfactory conditions have been corrected.

edit note:  Use the following preparation article for adhesive applied installations only.

preparation

Prior to installing ceiling panels, make certain that surfaces to which adhesive will be applied are clean and free of dust, dirt, and other residues that would inhibit a proper bond.

INSTALLATION

Comply with manufacturer’s instructions and recommendations for installation of acoustical panels:

Coordinate with mechanical and electrical in locating and spacing fixtures, diffusers, and similar items located in ceiling.

Lay out pattern per reflected ceiling drawings.  Where not otherwise indicated, lay out in such manner that margins on opposite sides of rooms are equal or greater than 1/2 tile in width.

Where acoustical ceilings of different heights abut, install acoustical material matching ceiling at vertical surface at ceiling break match ceiling, unless otherwise indicated.

Suspension system:  Refer to Section 09 53 00 – Acoustical Ceiling Suspension Assemblies for installation requirements.

or

Suspension System:  [Architect to insert acoustical tile ceiling system suspension system installation requirements here.]

Acoustical Panels:

Refer to manufacturer’s written installation instructions.

Install lay in acoustical ceiling panels flush and level in suspension system.

Install panels with hand protection to avoid soiling.

Press panels from above to set into grids.  Do not pull from face.

CLEANing

Clean adjacent surfaces and remove unused product and debris from site.

After installation is completed, clean soiled surfaces of materials.

Remove and reinstall improperly installed material.

Remove damaged or discolored material, or material that cannot be properly cleaned, and install new material.

END OF SECTION

willtec®  is a product of pinta acoustic, inc.